## Slide 1: A Prototype of a Machine Learning Workflow to Classify Land Use from the Housing Market Dynamics
MASc final presentation
Presented by: Stepan Oskin
Supervisor: Erik J Miller
Date: 20-Sep-2019
Notes: Growth centers
West Don Lands
Liberty village
Riverdale
Outline
Deadline to submit thesis
Month-by-month tuition

## Slide 2
Section 1:
Background

## Slide 3
Stepan Oskin, Master of Applied Science candidate at the
Department of Civil Engineering
Undergraduate degree in Mechanical Engineering
from St. Petersburg State Polytechnic University (Russia)
Started my studies at UofT in the MEngCEM program,
focused on Energy, switched to MASc focused on Data Science
After 2 terms of MEngCEM, switched to MASc inspired by
complexity studies (CEM1004)
Started my thesis under the supervision of Eric Miller,
interested in the interaction of urban systems
1.1. Personal background

## Slide 4
Under the supervision of Eric Miller, became a part of the team at the UTTRI
Spent the past year “untangling” a large historical dataset of real estate transactions (Teranet)
Designed and implemented a machine learning workflow to dynamically classify land use at a parcel level based on the housing market dynamics and Census data – primary focus of this master’s thesis
1.1. Personal background (cont.)

## Slide 5
1.2. Land use and transportation research
Source: Eric J Miller, David S Kriger, and John Douglas Hunt. Integrated Urban Models for Simulation of Transit and Land Use Policies Guidelines for Implementation and Use. 1998.
An Idealized Integrated Urban Model System:

## Slide 6
1.3. Evolution of LUT models
Source: Michael Iacono, David Levinson, and Ahmed El-Geneidy. Models of transportation and land use change: A guide to the territory. Journal of Planning Literature, 2008.

## Slide 7
1.4. Motivation
Microsimulation models are “data-hungry”
Disaggregation of models is mirrored by disaggregation of data sources (Census/TTS vs Teranet)
Fine-scale housing market dynamics, heterogeneity of the GTHA housing market
“Lack and abundance” paradox: Teranet’s dataset provides a wealth of data with a lack of features

## Slide 8
1.5 Teranet’s dataset of land registration records

## Slide 9
1.6. Teranet: challenges and opportunities
Challenges:
  Size of Teranet’s dataset, computational requirements
  Lack of features
  No ability of differentiating transactions by property type
  Opportunities:
    Date and location information allows joining different data sources and engineering new features
    Department of Geography has manually collected detailed land use information in 2012 and 2013
    Machine learning to classify land use from housing market

## Slide 10
1.7. Objectives of this work
Land use from different sources (DMTI, Dept. of Geography) can be used to separate Teranet transactions by property types
If consistent and meaningful labels can be produced from land use, machine learning can be used to predict land use changes based on the housing market behaviour:
  dynamically (recognizing changes real-time)
  at a parcel level
  with a high degree of accuracy

## Slide 11
Section 3:
Data sources

## Slide 12
3.1 Relationship between datasets
DMTI
Land Use
Teranet
EPOI
fk: pin_lu
many
pk: PIN
one
many
fk: PIN
one
fk: dauid
DA-level data
Census
Parcel-level data
pk: dauid
TAZ-level data
fk: taz_o
postal-code-level data
fk: pca_id
FSA-level data
fk: fsa
time-indexed data
fk: year
many
many
one
one
pk: dauid
many
many
many
pk: transaction_id
Fuel prices
TTS
variables
Inflation
coefs.
one
pk: year
municipality-level data
fk: csduid
pk: PIN
many
Geog.
Land Use

## Slide 13
2.1. Data sources used
Teranet
Select Census variables
Select TTS variables
DMTI land use
Detailed land use (Department of Geography)

## Slide 14
2.2. Spatial units used by different sources
Teranet: point (parcel centroid)
Select Census variables: DA polygon
Select TTS variables: TAZ polygon (2001 zone system)
DMTI land use: parcel
Detailed land use (Department of Geography): parcel

## Slide 15
2.3. Matching spatial units
Challenges:
Spatially joining polygon-based data is challenging
Combining sources needs spatial joins to connect primary keys or area weighted spatial interpolation of data to a common unit of analysis
Boundaries may change over time
Proposed solution:
Relate all polygon-based data to time-indexed points
Polygon-based Census and TTS data can be joined to Teranet points with respect to temporal relationships (discussed next)

## Slide 16
2.4. Temporal spans of different sources
Teranet: timestamp (date)
Select Census variables: once in 5 years
Select TTS variables: once in 5 years
DMTI land use: 2001-2014, by year
Detailed land use (Department of Geography): 2011-2012

## Slide 17
2.4. Temporal spans of different sources
Teranet: (...)1985-2017
Select Census variables: ...2001, 2006, 2011, 2016
Select TTS variables: 1986, ... , 2001, 2006, 2011, 2016
DMTI land use: 2001-2014, by year
Detailed land use (Department of Geography): 2011-2012

## Slide 18
2.4. Temporal spans of different sources
DATA SOURCES | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Census |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TTS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
DMTI land use |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
DMTI postal codes |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
DMTI EPOI |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
EMME network calculations |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Teranet |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Dept of Geography land use |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Fuel price in Toronto |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 19
2.5. Matching temporal spans
Challenges:
Discrete vs “continuous” measurements
Census and TTS variables are sampled once every 5 years, while Teranet data is recorded daily
Urban form is continuously evolving
Land use information can become inaccurate with time
Aggregation or interpolation required
Aggregation or interpolation is required to match the different data sources used for longitudinal studies

## Slide 20
2.5. Matching temporal spans
Proposed solution (options):
Direct match
  Use only subsets of Teranet records for appropriate Census/TTS year
  Benefits: precision of measurement
  Disadvantages: limited use of Teranet
Interpolate discrete measurements
  Census / TTS variables can be turned into continuous via interpolation
  Benefits: closest match by time
  Disadvantages: more assumptions
Assign Census/TTS temporal spans to Teranet records
  Each Census / TTS survey can be assigned a temporal span of 5 years
  Benefits: avoid interpolation – less assumptions and preprocessing
  Disadvantages: step-change in Census/TTS variables, varying accuracy

## Slide 21
2.5. Matching temporal spans
DATA SOURCES | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Census |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TTS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
DMTI land use |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
DMTI postal codes |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
DMTI EPOI |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
EMME network calculations |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Teranet |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Dept of Geography land use |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Fuel price in Toronto |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Each Census / TTS year gets assigned a 5-year span
to match to Teranet records.

## Slide 22
Section 3:
Data preparation

## Slide 23
Land use
Land use
3.1 Data preparation: all data sources
Teranet dataset
Spatial joins
Correct for
consistency
price > 10’000 CAD,
new attributes
Select Census variables
Teranet
Census
Select TTS variables
TTS
Land use
DMTI
GTA land use
Geo department
Hamilton
land use
GTA + Hamilton
Land use
GTHA land use
Concat
Spatial joins
Tidy
Tidy
Convert Hamilton to GTA codes
points
DA-level
TAZ-level
parcel-level
parcel-level
Classification
algorithm

## Slide 24
Correct
for
consist-ency
Raw
Teranet
data
Add foreign
keys via spatial joins
Add new attributes
0.
1.
final
3.
2.
3.2. Teranet data preparation
Encode target classes,
join with Census / TTS variables
4.
Classification
algorithm
Predicted
land use
Raw Teranet data:
9,039,241 rows
15 columns
Augmented and filtered
Teranet data:
5,188,513 rows
79 columns

## Slide 25
3.3. Outliers
Bottom outliers: records with price < 10’000 CAD removed.

## Slide 26
3.3. Outliers
Top outliers “peeled” in layers: 7 different criteria used
`outlier_xy_2`:

## Slide 27
3.3. Outliers
Top outliers “peeled” in layers: 7 different criteria used
`outlier_xy_10`:

## Slide 28
Section 4:
Land use classes

## Slide 29
4. Land uses classes (target variable)
The top 10 land use categories (by frequency) from detailed land use are regrouped into 4 target classes:
“detached”: Single Detached House
“duplex_townhouse”: Duplex/Semi-Detached or Townhouse
“condo”: Apartments/Condos/Residence or Strata Townhouses
“other”: mixed, commercial, industrial, and everything else

## Slide 30
4. Land use class 1: detached

## Slide 31
4. Land use class 2: duplex/townhouse

## Slide 32
4. Land use class 2: duplex/townhouse

## Slide 33
4. Land use class 3: condo / strata

## Slide 34
4. Land use class 3: condo / strata

## Slide 35
4. Land use class 4: other (examples)

## Slide 36
4. Land use class 4: other (examples)

## Slide 37
Section 5:
Feature selection

## Slide 38
Data preparation step
augmented Teranet dataset
from 4 features to 64:
5.1. Augmented data
'lro_num’,
'pin', 'consideration_amt', 'registration_date', 'POSTAL_CODE', 'PROVINCE’,
'UNITNO', 'STREET_NAME', 'STREET_DESIGNATION', 'STREET_DIRECTION', 'MUNICIPALITY', 'STREET_SUFFIX', 'STREET_NUMBER’,
'X', 'Y'

## Slide 39
5.2. Feature selection: PCA and Random Forest
PCA:

## Slide 40
5.3. Feature selection: SBS algorithm
Sequential Backward Selection (SBS) algorithm determined 9 features most relevant to models

## Slide 41
5.3. Feature selection: SBS algorithm
Sequential Backward Selection (SBS) algorithm determined 9 features most relevant to models

## Slide 42
5.4. Feature selection: dimensionality reduction
PCA and LDA were attempted but did not offer sufficient improvement
PCA (KNN)
LDA

## Slide 43
Section 6:
Classification

## Slide 44
5.5. Train-test-validation split
Subset of records from 2012 used to train and test model (70-30 random split)
Records from 2011 and 2012 are used to validate predictions

## Slide 45
6.1. Classification algorithms attempted
Perceptron
Logistic regression
Decision Tree
K-Nearest Neighbors

## Slide 46
6.2. Best preforming algorithm: Random Forest
Best performance on all 64 features:
Random Forest

## Slide 47
6.2. Best preforming algorithm: Random Forest
Best performance on all 64 features: 94-95% on validation
Best performance on 9 features from SBS: 91-93% on validation
Used to produce new attribute `lucr_predict_af`
Used to produce new attribute `lucr_predict_9f`

## Slide 48
6.2. Best preforming algorithm: Random Forest
Random Forest classification algorithm offers
the best performance:
Best accuracy (94-95% on validation sets with all features)
Computational efficiency
Easily parallelized “out-of-the-box” in scikit-learn
Scalable

## Slide 49
Section 7:
Results

## Slide 50
7.1. Detailed land use joined to Teranet records

## Slide 51
7.1. DMTI vs Department of Geography
Land use from the Department of Geography is
more detailed and more accurate (but limited in time)

## Slide 52
7.2. Predicted land use added as a new feature

## Slide 53
7.2. Department of Geography vs predicted
Points are colored
by predicted land use

## Slide 54
Land use
Land use
7.3 Results are stored as a database
Teranet dataset
Spatial joins
Correct for
consistency
price > 10’000 CAD,
new attributes
Select Census variables
Teranet
Census
Select TTS variables
TTS
Land use
DMTI
GTA land use
Geo department
Hamilton
land use
GTA + Hamilton
Land use
GTHA land use
Concat
Spatial joins
Tidy
Tidy
Convert Hamilton to GTA codes
points
DA-level
TAZ-level
parcel-level
parcel-level
Classification
algorithm
Add to the database
PostgreSQL

## Slide 55
7.3. Entity relationship (ER) diagram
PIN-level data
(e.g., land use,
EPOI, etc.)
Postal-code
level data
FSA-level
data
TAZ-level data
DA-level data
(e.g., select
Census variables)
Time-indexed
data
(e.g., fuel prices)
Teranet dataset is related to multiple groups of datasets
based on different spatial and temporal relationships.

## Slide 56
7.3 SQL example: join different datasets
PIN-level data
(e.g., land use,
EPOI, etc.)
Postal-code
level data
FSA-level
data
TAZ-level data
DA-level data
(e.g., select
Census variables)
Time-indexed
data
(e.g., fuel prices)
This query joins attributes from various data sources at Teranet transaction level:
Select variables and specify column names
Join data sources

## Slide 57
Section 7:
Conclusion

## Slide 58
7. Conclusion
Land use from different sources can be used to separate Teranet transactions by property types
If consistent and meaningful labels are produced from Dept. of Geography’s land use, machine learning can be used to predict land use changes based on the housing market behaviour:
  dynamically (recognizing changes real-time)
  at a parcel level
  with a high degree of accuracy

## Slide 59
Thank you!
Questions?

## Slide 60
Appendix

## Slide 61
GTHA
DA-level
Profiles of Income
2016 Census
9,182 rows
218 columns
polygons
DA-level
Profiles of Income
2016 Census
Esri Open
Data Portal (*)
da_census_income_obtain.ipynb
(*) https://opendata.arcgis.com/datasets/9d262f8a576842fbb2afbc8c51a64178_1.geojson
data/da_census/da_census_income.csv
Teranet
data/teranet/HHSaleHistory.csv
Spatial
join #1
how=‘inner’,
op=‘within’
data/teranet/1.1_Teranet_DA.csv
Add columns
'DAUID', 'CSDUID', 'CSDNAME'
Raw
Teranet dataset
9,039,241 rows
15 columns
points
Teranet,
filtered for GTHA,
+DA keys
6,803,691 rows
18 columns
points
Transportation
Analysis Zones
(TAZ)
GTHA
TAZ geometry and general info
1,716 rows
5 columns
polygons
data/da_census/da_census_income.csv
Spatial
join #2
how=‘left’,
op=‘within’
2.1.1_teranet_gtha_da_spatial_join.ipynb
taz_info_obtain.ipynb
2.1.2_teranet_taz_spatial_join.ipynb
Teranet,
filtered for GTHA,
+DA, TAZ keys
6,803,756 rows
19 columns
points
Add column
'TAZ_O'
Forward
Sortation Areas
(FSA)
Canada
FSA geometry
1,614 rows
4 columns
polygons
Spatial
join #3.1
how=‘left’,
op=‘within’
Download from library website (**)
2.1.3_teranet_pg_fsa_spatial_join.ipynb
Teranet,
filtered for GTHA,
+DA, TAZ,
FSA keys
6,803,756 rows
24 columns
points
Add column
‘FSA'
https://mdl.library.utoronto.ca/collections/geospatial-data/platinum-postal-code-suite-4
DMTI
Census
Teranet
Parcel-level
Land Use
for GTA
and Hamilton
GTHA
parcel-level land use
1,664,862 rows
18 columns
polygons
Spatial
join #4
how=‘left’,
op=‘within’
lu_obtain.ipynb
Teranet dataset,
filtered for GTHA,
+DA, TAZ, FSA, PCA_ID, pin_lu keys
6,803,767 rows
27 columns
points
Geography
dept.
Received from Teranet
2.1.4_teranet_lu_spatial_join.ipynb
data/teranet/1.2_Teranet_DA_TAZ.csv
data/teranet/1.3_Teranet_DA_TAZ_PG_FSA.csv
data/teranet/1.4_Teranet_DA_TAZ_FSA_LU.csv
Add columns: ‘pin_lu', ‘LANDUSE', ‘PROP_CODE'
2.1 Teranet Spatial joins
Ontario
Postal Code Geography
555,668 rows
12 columns
polygons
Spatial
join #3.2
how=‘left’,
op=‘within’
Add columns
‘PCA_ID', ‘postal_code_dmti’,
‘MAF_ID’, ‘DEL_M_ID'
Postal Code
Geography
TAZ/TTS

## Slide 62
Correct
for
consistency
Raw
Teranet
data
Add to the database
Add foreign
keys via spatial joins
Add new attributes
HHSaleHistory.csv
1.1_Teranet_DA.csv
1.2_Teranet_DA_TAZ.csv
1.3_Teranet_DA_TAZ_FSA.csv
1.4_Teranet_DA_TAZ_FSA_LU.csv
2_Teranet_consistent.csv
3_Teranet_new_cols.csv
3_Teranet_nonan_new_cols.csv
PostgreSQL
0.
1.
2.
final
3.
2.1.1_teranet_gtha_da_spatial_join.ipynb
2.1.2_teranet_taz_spatial_join.ipynb
2.1.3_teranet_pg_fsa_spatial_join.ipynb
2.1.4_teranet_lu_spatial_join.ipynb
2.2_teranet_consistency.ipynb
2.3_teranet_new_cols.ipynb
2.3_teranet_nonan_new_cols.ipynb
2. Teranet preparation data flow
(4.) Remove duplicates
(pending)